## Slide 1: Pertemuan 5 Storage Devices

## Slide 2: HDD (Hard Disk)
Komponen fisik
Platters
Read/write head
Actuator
Actuator arm and axis
Komponen logika
Tracks
Sectors
Clusters
Files

## Slide 3: Hal yang perlu diperhatikan saat membeli hard disk
Ukuran
Interface
Rotational speed (RPM)
SEEK TIME juga penting !!

## Slide 4: Hard Drive Interfaces
Integrated Drive Electronics (IDE).
Advanced Technology Attachment (ATA ).
Extended IDE (EI DE) and ATA -2.
ATA Packet Interface (ATAPI)
Paralel ATA (PATA)
Serial ATA (SATA)

## Slide 5: PATA
Menggunakan DMA untuk direct-transfer (tidak merepotkan CPU

## Slide 6: PATA CONNECTOR & KABEL

## Slide 7: Konfigurasi master dan slave

## Slide 8: PATA Power
Standard 4-pin Molex connector :
  Yellow 12 V
  Black ground (kabel tengah)
  Red 5 V

## Slide 9: Serial vs Paralel
Lebih cepat yang mana?
LVD Signaling

## Slide 10: SATA versions
SATA 3G adalah generasi SATA 2

## Slide 11: SATA connectors

## Slide 12: SATA Power Connector & Cables
Orange—3.3 V
Black—Ground
Red—5 V
Black—Ground Yellow—12 V

## Slide 13: Hot-swappable
You can plug in or remove the drive while the system is powered on.

## Slide 14: Small Computer System Interface (SCSI)
SCSI-1 (50 pin cable, transfer rate 5 MBps, 8 bit bus, support max. 8 devices)
SCSI-2 (25, 50 dan 68 pin, transfer rate 10 MBps, 8 bit bus)
Fast-Wide SCSI (16 bit bus, support max 16 devices, transfer rate 16 MBps)
SCSI-3 / Ultra SCSI (50, 68 dan 80 pin)

## Slide 15: Tipe Ultra SCSI

## Slide 16: SCSI Interfaces
25 pin
50 pin
68 pin
80 pin

## Slide 17: SCSI IDs
SCSI devices diatur oleh SCSI controller.
Setiap SCSI devices (termasuk controller) punya ID
Prioritas tertinggi = 7, prioritas terendah = 0;
Ketika SCSI support 16 devices, prioritas awal tidaj berubah: prioritas tertinggi = 7, prioritas terendah = 0 ;
ada penambahan 8 – 15: untuk prioritas tertinggi = 15,
prioritas terendah = 8
urutan dari prioritas tertinggi adalah sebagai berikut :
7,6,5,4,3,2,1,15,14,13,12,11,10,9,8

## Slide 18: Assign SCSI ID
Caranya assign ID adalah dengan mengatur 4 jumper.
Keempat jumper tersebut merepresentasikan ID dalam bilangan biner (jumper 3 = , jumper 2 = ,
jumper 1= , jumper 0 = )
Jumper terpasang = 1 ; jumper lepas = 0
Contoh untuk assign ID = 7 , bilangan binernya = 0111,
Maka lepas jumper 3 untuk merepresentasikan 0.

## Slide 19: SCSI binary value

## Slide 20: Daisy chaining

## Slide 21: External Connection Types
USB (USD 2.0 support 480 Mbit/s;
USB 3.0 support 5 Gbit/s, max
cable 5m, max 127 devices on
single USB hub)

## Slide 22: External Connection Types
Firewire (IEEE 1394)
Firewire 400 (1394a) speeds up to 400 Mbps
Firewire 800 (1394b) speeds up to 800 Mbps
max cable 4,5 m
max daisy chain on single port = 63
Firewire port : 4,6,9 pin

## Slide 23: External Connection Types
eSATA
Based on SATA 3G
Transfer rate up to 3 Gbit/s
Have 7 wires and shielded
Max cable 2 m
Can only connect to 1 device to the port

## Slide 24: External Connection Types
eSATAp
Kombinasi SATA dan USB
Bisa detect keduanya
7 pin (SATA) , 4 pin (USB)
Originally support 5V powered device tapi ada tambahan 2 pin untuk mengakomodasi 12V powered device

## Slide 26: Ethernet
RJ-45

## Slide 27: Solid State Drives (SSD)
Tidak memiliki komponen bergerak
Nonvolatile

## Slide 28: Flash memory
Compact Flash (CF)
Secure Digital (SD)
Mini-SD
Micro-SD
xD

## Slide 29: Optical Disk and Drive

## Slide 30: Compact Disk Operation

## Slide 31
R (Recordable)
RW (Rewriteable)
RE ( Recordable Erasable)
Speed
CD: 150 KBps
DVD: 1.39 MBps
Blu-Ray: 4.5 MBps

## Slide 32: Penyimpan lainnya
Floppy disk
Tape disk

## Slide 33: Redundant Array of Independent (or Inexpensive) Disks (RAID)
uses multiple disks to provide increased performance and fault tolerance.

## Slide 34: RAID 0
Membagi data ke seluruh disk
Akses ke data lebih cepat
Ketika ada kesalahan, data tetap hilang

## Slide 35: RAID 1
Mirroring
Jika data pada disk 1 hilang, maka data yang sama di disk lain masih ada

## Slide 36: RAID 5
Menggunakan minimal 3 disk.
Diberikan alokasi tempat pada ketiga disk setara dengan 1 disk khusus untuk parity

## Slide 37: Contoh parity ganjil dgn RAID 5

## Slide 38: RAID 10
Kombinasi dari RAID 1 dan RAID 0

## Slide 39: Ruang penyimpanan yang dapat digunakan untuk menyimpan data pada RAID

## Slide 40: RAID

## Slide 41: Masalah umum pada harddisk
Loud Clicking Noise
Read/Write Failure
Slow Performance
Failure to Boot

## Slide 42: THANKS!
Any questions?